## Slide 1
QSM:
Quantitative Susceptiblity Mapping
Henrique Azevedo
josehenrique@usp.br
InBrain Workshop
ppm

## Slide 2
Introduction

## Slide 3
Quantitative Susceptibilty Mapping1
Tissue’s bulk magnetic susceptibilty in vivo
Four major contributors: water, myelin, iron and calcium.
Trends in Neurosc. 42 (2019) 384-401
1 Z. Med. Phys. 26 (2016) 6-34

## Slide 4
QSM applications
Asses beta amyloid agregation and iron accumulation in Alzheimer’s disease
T2*-weighted
QSM
Amyloid-beta
tau
iron

## Slide 5
QSM applications
QSM value is positively correlated with scale that measures the progression of Parkinson disease

## Slide 6
QSM applications
QSM to characterize oxygen saturation non-invasively in heart
QSM to characterize medial cartillage damage in knee

## Slide 7
How to measure susceptibilty with MRI?

## Slide 8
Susceptibility source
Field pertubation
How to measure susceptibilty with MRI?
B0

## Slide 9
Susceptibility source
Field pertubation
Dipole field
How to measure susceptibilty with MRI?

## Slide 10
Suscep. source
Dipole
Field distrib.
-1
Dipole
Suscep. source
Field distrib.
Fourier Transform of Field distrib.
Fourier Transform of Susc. Source
/

## Slide 11
-1
Dipole
Suscep. source
Field distrib.
Convolution
theorem

## Slide 12
QSM pipeline

## Slide 13
QSM processing steps

## Slide 14
Hands - on

## Slide 15
Knowning the data
Magnitude – magnitude images at 4 echos
Phase – phase images at 4 echos
Mask – mask of the brain
Sepia_header – informations such as echo times (TE) , magnetic field strenght in Tesla, orientation of the aquicsition.
https://drive.google.com/drive/folders/1ACVtOer_pq7_Y_Mnj4u4ML-w_5HYfpJQ?usp=sharing

## Slide 16
MEDI toolbox: http://pre.weill.cornell.edu/mri/pages/qsm.html
“/usr/local/inbrain/QSM_toolbox/MEDI_toolbox”

## Slide 17
Magnetic field strenght (T)
Magnetic field Direction (x, y, z)
Frequency - B0*gamma (Hz)
Echo spacing (s)
Image matrix size
Echo times (s)
Spatial resultion (mm)
Information to obtain maps with correct units

## Slide 18
Load the data at Matlab workspace
https://drive.google.com/drive/folders/1ACVtOer_pq7_Y_Mnj4u4ML-w_5HYfpJQ?usp=sharing

## Slide 19
View the data
Terminal de comando  “itksnap”
ITK-SNAP  File  Open Main Image  Browse...
“/usr/local/inbrain/QSM_Data/Data_1”

## Slide 20
View the data

## Slide 21
Phase unwrapping
The “wraps” occurs because phase information is restrained to [-π, π] interval
Every time that phase value lays outised this interval an addition or subtraction of π is done

## Slide 22
Phase unwrapping
First step – Nonlinear fit of phase between echos
Second step – Spatial unwrap of phase
Thrid step – Field map

## Slide 23
Phase unwrapping
MEDI nonlinear fit
Phase wraps over echos times are removed to estimate the slope of phase variation over time and the correspondign value of ΔB
Phase unwrapping: Laplacian (MEDI)
The resultant phase was spatially unwrapped using Laplacian operator formulation.

## Slide 24
Background field removal
=
+

## Slide 25
Background field removal

## Slide 26
Background field removal
Projection onto Dipole Field (PDF)
Magnetic field for a dipole outside a ROI is approximately orthogonal to the magnetic field of a dipole inside the ROI.
Bbck
Bint
B = Bint+ Bbck

## Slide 27
Quantitative susceptibilty
mapping

## Slide 28
Quantitative susceptibilty
mapping
Morphology Enabled Dipole Inverse (MEDI)
Edges in susceptibilty are nearly the same as magnitude images obtained at the same acquisition.
Employ a weighted l1 minimization method that penalize susceptibilty values at those voxels that are not part of magnetization image

## Slide 29
THANK YOU!

## Slide 30
SEPIA toolbox
https://github.com/kschan0214/sepia
Download:
Documentation:
https://sepia-documentation.readthedocs.io/en/latest/

## Slide 31
In MATLAB: Set Path  Add Folder  sepia/directory  Save
In MATLAB: type “sepia” on Command Window and click enter

## Slide 32
In SEPIA: Utility Manage Dependency  Add directory for each toolbox